## Slide 1: Modern Control Theory
Model Predictive Control - MPC – Lecture 2
Dynamic Prediction Models

## Slide 2: RECAP
KEY ELEMENTS OF MPC
Prediction Model
  Effect of past actions onto the future (implemented)
  Effect of current and future actions (to be implemented)
Objectives with Constraints to be met on Input action, Output deviations
Optimizer to obtain the control actions
Second definition of MPC:
MPC is a controller which uses prediction that includes the effect of past and future control actions such that to satisfy the desired objectives without violation of constraints but implements only the first time-step action at EVERY TIME STEP.
Implementing the first step and re-computing the control trajectory at each time step is called Receding Horizon control

## Slide 3: Receding Horizon Control

## Slide 4: Receding Horizon Control

## Slide 5
Receding Horizon Control

## Slide 6
Receding Horizon Control

## Slide 7: Receding Horizon Control/ MPC
Implementation steps ONLINE
Obtain the current measurements of states
Compute the optimal finite horizon control sequence (uk, uk+1, …uM)
Implement first move uk
Repeat from Step 1
What are offline activities for a MPC controller?
MPC Controller
at each time step (k)
Past inputs
Current measurements
past measurements
Model
Objectives
Constraints
Tuning
Identifying a model – system identification – 60-70% of effort
Identifying the objectives and cost function
Tuning
uk, uk+1, …uM

## Slide 8: Prediction models in MPC

## Slide 9: Dynamic prediction models
Model types
Physics/ first principles based
Data-based (or empirical) models
Input/ Output Relationships
Linear (L) or
non-linear (NL)
Types of LINEAR models
Impulse response coefficients (Linear, Stable, data based)
Step response coefficients – Large industry adoption (Linear, Stable, data based)
State-space – Recent applications such autonomous vehicles, robots, satellite systems (Linear, Non-linear, Stable/ Unstable, physics and data based)

## Slide 10: Discrete impulse response models

## Slide 11: Step Response models (1/4)
Why are step responses popular?
Duk = uk – uk-1
uk-1 = 0
uk = 1
y1 = y0 + S1Du0
y2 = y0 + S2Du0 . .
.
yn = y0 + SnDu0
For a unit step uk = 1 for all k

## Slide 12: Step response predictions (2/4)
y1 = y0 + S1Du0
y2 = y0 + S2Du0 + S1Du1
y3 = y0 + S3Du0 + S2Du1
. .
. .
yN = y0 + SNDu0 + SN-1Du1
Can extend also to MIMO Systems as simple Multi input Single output (MISO) systems
From the Principle of Superposition for linear systems:

## Slide 13: Step response predictions (3/4)
Si = ith step response coefficient
Duk = u(k) – u(k-1)
N = prediction window or horizon
One step ahead prediction
Two step ahead prediction

## Slide 14: Step response prediction (4/4)
jth step ahead prediction
Predicted FREE response
=
What happens when u(k-i) = u(k-1) for all i > 0

## Slide 15: Example – simple predictive receding horizon controller
Find a predictive control law with single receding horizon move, such that
jth step ahead prediction
Given
j = J,
Du(k + i) = 0 for i > 0, i.e. Du(k + 1) = Du(k + 2) …. = Du(k + J-1) = 0
Forced response
Free response
ysp =
SISO system with prediction-based control law using simple step response coefficients
What are the pitfalls in this?

## Slide 16: Example – simple predictive receding horizon controller
The move required tend to be smaller as J increases
J = 3, 4, 6, 8
Dt = 5 mins
As J increases Sj increases
As J decreases, y becomes aggressive

## Slide 17: Multi input Multi output prediction models - step response (1/2)
Du(k + j-1)
Sj
Sj-1
S1
=
+

## Slide 18
Principle of superposition: Example 2 inputs and 2 outputs
Multi input Multi output prediction models - step response (2/2)
‘r’ inputs
‘m’ outputs
P step ahead predictions for M future control moves
Forced
response
Free
response