## Slide 1: Modern Control Theory
Model Predict Control - MPC – Lecture 9
Unconstrained Control move calculation - MIMO

## Slide 2: Prediction using State space models - MIMO
m inputs, q outputs and n1 states
For good control q <=m
w(k) is integrated white noise
Am is n1 x n1
Bm is n1 x m
Bd is n1 x m
Cm is q x n1
u is m x 1
y is q x 1
Augmented
‘q’ Integrators
Incremental form

## Slide 3: Prediction using State space models - MIMO
y(k+1) = C x(k)
System in incremental form
System
representation
Output Prediction equation
q*NpX 1
(q*Np x (n1+q)
q*Np x m*Nc
Output Prediction equation
m*Nc X 1

## Slide 4: Unconstrained solution – MIMO
Now
=
+
= 0
FT (Rs – F(ki))
^
Solving for DU we get
DU = (FTF + R)-1FT (Rs – F(ki))
Implementation steps ONLINE
Obtain the current measurements of states,
Estimate the states using Kalman filter
Compute the optimal finite horizon control sequence (uk, uk+1, …uM)
Implement first move uk for each of the inputs
Repeat from Step 1
uki = u (ki-1) + Duki
(FTF+ R)DU =
(first m value in DU)

## Slide 5: Example problem
DU = (FTF + R)-1FT (Rs – F(ki))
Matrices to compute:
F, F, FTF, FT Rs , FT F
Linearize around some operating point (h1.h2), we get
Am
Level control of coupled tanks

## Slide 6: Demo
Sampling time = 0.05 secs, discretize
Np = 10, Nc = 3
Linearize around L1 = 4m, L2 = 3.5m

## Slide 7: Handling constraints
Inputs
Rate of change constraints on the input – (Du)
Absolute constraint (u)
Output
Output limits - y
Inputs – Hard constraints – cannot be violated
Output – Soft constraints – violation allowed with some penalty

## Slide 8: Handling input constrains – Amplitude of control signal u
Decision variable is Du
Example: SISO Nc = 4
C1
C2
-

## Slide 9: Handling input constraints - incremental change in inputs
Rate of input change: Most easy constraint to include
Decision variable is Du

## Slide 10: Handling output constraints – control limits
y1min < y1pred (k)< y1max
y2min < y2pred (k)< y2max
….
yqmin < yqpred (k)< yqmax
Ymin < Ypred (k) < Ymax
Ymin < Ypred (k+1) < Ymax
…
Ymin < Ypred (k+Np) < Ymax
Ypred = Fx(ki) + FDU

## Slide 11: SISO Example – input constraints
Nc = 3

## Slide 12: Handling constrains
Min
Du
Min
Du
Min
Du
J/2 =
½ DUT (FTF+ R)DU -DUTFT (Rs – F(ki))
Min
Du
J’= ½ DUT EDU + DUT G
This is standard Quadratic programming (QP) with
E called the Hessian – symmetric positive definite
Subject to
Input amplitude
Input rate of change
Output rate of change
Linear in constraints
E = FTF+ R
G = FT (Rs – F(ki))

## Slide 13: Solving QP problem
Active set method based on Lagrange multipliers
Interior point methods