## Slide 1: Modern Control Theory
Model Predict Control - MPC – Lecture 11
Constrained Control move calculation - MIMO

## Slide 2: Handling constraints
Inputs
Rate of change constraints on the input – (Du)
Absolute constraint (u)
Output
Output limits - y
Inputs – Hard constraints – cannot be violated
Output – Soft constraints – violation allowed with some penalty

## Slide 3: Handling constrains
Min
Du
Min
Du
Min
Du
J/2 =
½ DUT (FTF+ R)DU -DUTFT (Rs – F(ki))
Min
Du
J’= ½ DUT EDU + DUT f
This is standard Quadratic programming (QP) with
E called the Hessian – symmetric positive definite
Subject to
Input amplitude
Input rate of change
Output rate of change
Linear in constraints
H = FTF+ R
f = FT (Rs – F(ki))

## Slide 4: Example problem
DU = (FTF + R)-1FT (Rs – F(ki))
Matrices to compute:
F, F, FTF, FT Rs , FT F
Linearize around some operating point (h1.h2), we get
Am
Level control of coupled tanks

## Slide 5: Demo
Sampling time = 0.05 secs, discretize
Np = 10, Nc = 3
Input constraints
  Low limit – U1, U2, Du1, Du2
  High limit – U1, U2, Du1, Du2
Linearize around L1 = 4m, L2 = 3.5m

## Slide 6: Impact of tuning – SISO system
With fixed control horizon Nc,
Increasing Np will slow down the system
With fixed prediction horizon Np,
Increasing Nc speeds the system
With fixed Np and Nc
Increasing the move weight, slows down the system
General Rule
Nc should be large enough
Np-Nc should be close to settling time of the system

## Slide 7: Closed loop analysis in Unconstrained MPC
Recall DU = (FTF + R)-1FT (Rs – F(ki))
Ky = First element of (FTF + R)-1FT Rs
Kmpc = First element of (FTF + R)-1FTF
Recall Incremental model
Closed loop Eigen Values are

## Slide 8: Closed loop stability example
DU = (FTF + R)-1FT (Rs – F(ki))
Case 1: No constraint on U R= 0
Du = [7.2 -6.4 0 0]
Case 1: Eigen Values
Case 2: constraint on U R= 10
Du = [0.127 0.103 0.083 0.07]
Case 2: Eigen Values
System has become slower

## Slide 9: Handling input constraints - incremental change in inputs
Rate of input change: Most easy constraint to include
Decision variable is Du

## Slide 10: Handling input constrains – Amplitude of control signal u
Decision variable is Du
Example: SISO Nc = 4
C1
C2
-

## Slide 11: Handling output constraints – control limits
y1min < y1pred (k)< y1max
y2min < y2pred (k)< y2max
….
yqmin < yqpred (k)< yqmax
Ymin < Ypred (k) < Ymax
Ymin < Ypred (k+1) < Ymax
…
Ymin < Ypred (k+Np) < Ymax
Ypred = Fx(ki) + FDU